SPREE LOG SHEET	INSTALLATION	Station:______________

Date:______________ Julian:____________ Time, GMT:_______________ Local:________________
Field Team:__________________________________________________________________________
GPS Location of Site: lat:____________ lon:_____________ elev(m):__________________
CONTACT/LANDOWNER:______________________________________________________________

EQUIPMENT
SENSOR TYPE:_______________________	SENSOR S/N:_____________________
DAS S/N: ____________________________	CLOCK S/N:________________
FLASH DISK 1 S/N:____________________	SIZE: _____________
FLASH DISK 2 S/N:____________________	SIZE: _____________

LOCATION OF HARDIG CASES_________________________________________________________
CHECK POWER SYSTEM (check while PV and battery NOT connected)
PV1: voltage: _________ current: __________ PV2: voltage: __________ current: __________
Bat 1: voltage:_________ chg. state: ________ Bat 2: voltage:_________ chg. state: ________
Were power checks done with batteries and solar panels disconnected? __________________________

INSTALL GURALP Declination used: _______________________
        MASS POSITION OFFSETS (NOTE: re-center if mass position offsets are more than 1.5 V)
	voltage (after finish of re-centering)	Attempts
VERT
N-S
E-W

INSTALL DAS
1: MODIFY RT130 PARAMETERS AND SEND TO DAS
   Work with Config -> load-> “spree-config”
   Edit station name and sensor serial #	->Send to DAS
2. CLEAR RAM (Control -> RAM -> Clear)
3. RESET SYSTEM (Control > Reset )

4. FORMAT FLASH DISK (Control -> Format Disk -> Disk 1: ❑ Disk 2: ❑

5. MONITOR: (Control -> Monitor -> stream 2 ->
ch 1: Midpt:__________ Range:____________ tap test: OK / NO
ch 2: Midpt:__________ Range:____________ tap test: OK / NO
ch 3: Midpt:__________ Range:____________ tap test: OK / NO

6. CHECK CLOCK STATUS (Contol -> Status -> GPS) (clock MUST lock BEFORE starting acquisition)
sec since LL: days:________:hr:________:min:________:sec:________

7. WRITE .CFG FILE TO DISK (Control>Status>DAS LP/WP-> WRITE) ................❑ YES ❑ NO

8. START ACQUISITION: (Control -> Status -> Start Acq)
        start time: days:________:hr:________:min:________:sec:________

9. VERIFY RAM INCREASING (Control -> Status -> Update): ....................................❑ YES ❑ NO

10. FORCE RAM DUMP to DISK (Control -> Ram -> Dump)
    verify RAM DECREASES and disk INCREASES (Control -> Status -> Update) .....❑ YES ❑ NO
Station:______________

11. BEFORE LEAVING SITE, RECHECK THE FOLLOWING TO ENSURE OPERATION
     DAS STATUS (Control -> Status)
Acq: Start ON/OFF
Events: ___________ RAM: _______ of _________ (Kb)
Disk 1 ___________ of ___________ Disk 2 ___________ of ___________
Temp: ___________ Power: input:____________ bkup chg:___________
ch: _________ DS:___________
    Make sure that all plugs and connections have been replaced - esp. SERIAL PORT

RECORD DIRECTIONS TO SITE AND ANY OTHER COMMENTS AND NOTES :