SPREE LOG SHEET	SERVICE	Station:______________

Date:______________ Julian:____________ Time, GMT:_______________ Local:_________________
Field Team:___________________________________________________________________________
STATION STATUS
Site Condition:________________________________________________________________________

DAS S/N: _________________________ CLOCK S/N:_____________
DAS STATUS (Control -> Status)
 Acq: Start ON/OFF
Events: ___________ RAM: _______ of _________ (Kb)
Disk 1 ___________ of ___________ Disk 2 ___________ of ___________
Temp: ___________ Power: input:____________ bkup chg:___________
ch: _________ DS:___________
CLOCK STATUS (Contol -> Status -> GPS)
sec since LL: days:________:hr:________:min:________:sec:_________
        phase diff: __________________________________________________

SENSOR STATUS: Sensor Type:______________ Sensor S/N:___________________
CENTER MASS POSITION OFFSETS
	Initial	Final	Attempts
Vertical
N-S
E-W

NOTE: re-center if mass position offsets are more than 1.5 V
MONITOR SENSOR: (Control -> Monitor -> stream 2 ->
ch 1: Midpt:__________ Range:____________ tap test: OK / NO
ch 2: Midpt:__________ Range:____________ tap test: OK / NO
ch 3: Midpt:__________ Range:____________ tap test: OK / NO

1. Calibrate Sensor (Control -> Aux. Control -> Test 1-3)	YES_______ NO________
2. Stop Acquisition (Control -> Status -> Stop Acq)
3. Disk Status (Control -> Status -> Update)
        Disk 1 ___________ of ___________ Disk 2 ___________ of ___________
4. Check power system: (check while PV and battery NOT connected)
PV1: voltage: _________ current: __________ PV2: voltage: __________ current: __________
Bat 1: voltage:_________ chg. state: ________ Bat 2: voltage:_________ chg. state: ________
Were power checks done with batteries and solar panels disconnected? __________________________

5. Get RT130 parameters from the DAS (Work with Config -> load -> from DAS) and check parameters

6. Record compact flash serial numbers before swap
Disk#1 S/N:______________ SIZE: _________Gb Disk #2 S/N:______________ SIZE: _________Gb

7. SWAP COMPACT FLASH CARDS AND RECORD NEW SERIAL NUMBERS after the swap
Disk#1 S/N:______________ SIZE: _________Gb Disk#2 S/N:______________ SIZE: _________Gb

8. CLEAR RAM (Control -> RAM -> Clear)

9. RESET SYSTEM (Control -> Reset)

10. FORMAT FLASH DISK (Control -> Format Disk -> Disk 1: ❑ Disk 2: ❑
Station:______________

11. WRITE .CFG FILE TO DISK (Control>Status>DAS LP/WP-> WRITE) ................❑ YES ❑ NO

12. CHECK CLOCK STATUS (Contol -> Status -> GPS) (clock MUST lock BEFORE starting acquisition)
sec since LL: days:________:hr:________:min:________:sec:________

13. START ACQUISITION: (Control -> Status -> Start Acq)
        start time: days:________:hr:________:min:________:sec:________

14. VERIFY RAM INCREASING (Control -> Status -> Update): ....................................❑ YES ❑ NO

15. FORCE RAM DUMP to DISK (Control -> Ram -> Dump)
    verify RAM DECREASES and disk INCREASES (Control -> Status -> Update) .....❑ YES ❑ NO

16. BEFORE LEAVING SITE, RECHECK THE FOLLOWING TO ENSURE OPERATION
     DAS STATUS (Control -> Status)
Acq: Start ON/OFF
Events: ___________ RAM: _______ of _________ (Kb)
Disk 1 ___________ of ___________ Disk 2 ___________ of ___________
Temp: ___________ Power: input:____________ bkup chg:___________
ch: _________ DS:___________
    Make sure that all plugs and connections have been replaced - esp. SERIAL PORT

RECORD OTHER COMMENTS AND NOTES: